## Slide 2
Outline
DSOC operational view
DSOC mission plan
System description
  Flight laser transceiver (FLT)
  Ground laser transmitter (GLT)
  Ground laser receiver (GLR)
  Mission operations system (MOS)
Downlink performance
Some pointing results
Uplink and link acquisition
Conclusions
Psyche Falcon Heavy launch Oct. 13, 2023

## Slide 3
INTRODUCTION
Communications data-rates increase with electromagnetic carrier frequency (decreasing wavelength)
Beam-Width ~ /D, where  is wavelength and D is the aperture diameter
Narrow laser beams deliver higher power density – translates to higher information rate
Use “optical communications,” “laser communications” and “lasercom” in this talk
Electromagnetic Spectrum
X-band
Ka-band
Lasers (near-infrared)

## Slide 4
NASA’s Need
04-4
Since Explorer 1 and Pioneer data-rates have increased by many orders of magnitude
“…Regardless of mission set scenario, average data rates will increase roughly two orders of magnitude over the next 20 years**…”
Future human exploration and high resolution science missions
  Higher data-rates will require increased bandwidth
  Non-NASA demands for bandwidth mount pressure on available radio frequency spectrum allocations
** DSN Future : A User Perspective, Dr. Les Deutsch, Deputy Director, Interplanetary Network Directorate, JPL, DSN 50th Anniversary Celebration Symposium, https://descanso.jpl.nasa.gov/dsn50th/dsn50th.html
Capabilities
  Streaming HD imagery
  Light Science
  Human Exploration of Deep Space
EARTH-ORBITAL
Occultation
Ranging
Interferometry
Streaming from MARS surface assets

## Slide 5
Table of NASA’s past and planned optical communications demonstrations
Name | Year | Distance (AU) | Data-Rate (Mb/s) | Mb/s  AU2
Lunar Laser Communications Demonstration (LLCD) on board LADEE spacecraft orbiting Moon | 2013 | 2.7E-3 | 622 Down 20 Up | 4.5E-3 Down 1.5E-4 Up
Optical Payload for Lasercom Science (OPALS) | 2014-2016 | 1.3E-5 | 50 Down | 8.5E-9
Laser Communications Relay Demonstration (LCRD) & ILLUMA-T | 2021-2023 | 2.7E-4 | 2440 Down/Up | 1.8E-4
Deep Space Optical Communications (DSOC) | 2022-2023 | 0.556 | 200 Down 0.0018 Up | 61.8 Down (demonstrated) 5.5E-4 Up
Terabyte Infrared Delivery (TBIRD), [not shown on previous slide] | 2022 | 1.3E-5 | 200000 | 3.4E-5
Optical-to-Orion | 2023 | 2.7E-3 | 80-260 Down 10-20 Up | 1.8E-3 Down 1.5E-4 Up
AU – Astronomical Units (1.496E8 Km)
Mb/s – Megabits per second
NASA’s Lasercom

## Slide 6
Ground Laser Receiver (GLR)
Palomar Mtn., CA
5m-dia. Hale Telescope
Ground Laser Transmitter (GLT)
Table Mtn., CA
1m-OCTL Telescope (5-7 kW Laser Power)
1064 nm uplink
Psyche
MOS
DSOC
MOS
~1550 nm downlink
Deep Space Network (DSN)
Advance NASA’s enhanced communication goals by:
Demonstrate optical communications from > 2 AU
Downlink data-rates 10  state-of-art telecommunications
Psyche
Spacecraft
(Launch 2023)
Deep Space Optical Communications (DSOC)
Optical Platform Assembly (OPA)
22 cm dia.
4 W Laser

## Slide 7
LAUNCH
October 13, 2023
EARTH
Approach
checkout
100d
May 2026
>5750 km
MARS
GRAVITY ASSIST
PSYCHE
CAPTURE
Aug 2029
MARS
Sep. 2025
Jan. 2025
Jul. 2024
Mission Summary
DSOC technology demonstration planned for 2 years of Psyche cruise
Link distances representative of Mars mission
Coordinated with Psyche Mission plans
End-to-end links demonstrated in the night sky
Sun-Earth-Probe angle
Sun-Probe-Earth angle
Earth-Psyche Distance
Sun-Psyche Distance
Night
Day
Night
No links planned
Sun-Earth-Probe Angle Outage
Psyche s/c Coasting
Psyche s/c Thrusting
Psyche s/c Coasting
Psyche s/c is here

## Slide 8
FLIGHT LASER TRANSCEIVER (FLT)

## Slide 9
High peak-to-average power laser
  4 W average power > 600 W of peak power
  Low jitter pulses 0.5, 1, 2, 4, 8 nanoseconds
  Two units built and qualified for space environment
Geiger Mode Avalanche Photo Diode Array Camera
  Operate avalanche photo diode biased above breakdown
  Single photon triggers an “avalanche” of carriers senses as an electrical pulse
Mark A. Itzler et al. SWIR Geiger Mode APD detectors for 3D Imaging
SPIE Proceedings, 2014
J. M. Dailey et al. High output power transmitter for high efficiency deep-space optical communications, Proc. SPIE, 2019
New Technologies on FLT (1 of 2)

## Slide 10
Optical Transceiver Assembly
Transmit Optical Path
Receive Optical Path
William Farr et al. IPN Progress Report, 2011
New Technologies on FLT (2 of 2)

## Slide 11
DSOC
Sun shade for solar protection of DSOC
  Integrated Optical transceiver Assembly (OTA, L3-Harris, SSG) with photon-counting camera (PCC from LL-MIT) and JPL electronics
      Tested, active TVAC, vibe and shock then delivered to JPL
  Advanced further integration and test at JPL
    Laser transmitter assembly (CACI)
    Isolation pointing assembly struts (Control Dynamics Inc.)
    Main electronics module with Universal Space Transponder heritage (JPL)
        Embedded Flight Software (FSW) and pointing control software (PCS)
    DSOC Accommodation Kit, DAK (JPL, First Mode)
  ATLO activities at JPL and Kennedy Space Center, Florida
Flight Laser Transceiver (FLT)

## Slide 12
GROUND LASER TRANSMITTER (GLT)

## Slide 13
Ground Laser Transmitter (GLT)
GLT Optics Assembly
To telescope
GLT Optics Bench
Uplink Laser Assembly
Assembled and tested 1064 nm laser rack (Fibertek Inc.)
  10 lasers 500 W each @ 25% duty cycle and 700 W each at 50% duty cycle
Integrated to OCTL telescope with custom optics (JPL)
  8 beams exit the telescope, at a time, to avoid irradiating telescope spiders
  Multi-beam laser beacon transmitted at 100 rad and 40 rad
  Minimized risk of damage to telescope mirrors
Installed and tested robust laser safety system for regulatory agency approval
  Guidance from JPL Safety Office
Tested and verified telescope “blind-pointing” for initial acquisition with predicts
Laser modulated with 2-PPM + 2-guard-band slots for 1.8 kb/s uses LDPC code
  Developed modulation electronics (JPL)
  Uplink sends commands in addition to serving as pointing reference beacon
Added downlink acquisition and communications receiver to GLT
  Spatially acquired downlink also allows “closed loop” GLT pointing
Optical-to-Orion (O2O) ground terminal at OCTL developed a photon counting receiver (PCR)
  Used DSOC design
  O2O PCR can be optically coupled to downlink and used bi-statically
Developed monitor and control system for comprehensive data and telemetry logging

## Slide 14
Outdoor Laser Safety System
2.3 km [MSL] OCTL altitude
5.5 km [MSL]
Tier 2: FAA Data Feed
18.3 km [MSL]
Tier 3: Predictive Avoidance File
Lasers will be shuttered below 20O elevation.
Tier 1 and 2 overlap region will be used to test reliability of tier 1 and 2.
Class A Airspace
Tier 1 purpose to detect non-interrogated aircrafts flying beneath the class A airspace.
4 thermal
2 visible
Tier 1: Thermal/Visible Cameras
Overlap Region

## Slide 15
Ground Laser Receiver (GLR)
Palomar Hale Telescope
Caltech Optical Observatories
https://sites.astro.caltech.edu/palomar/visitor/faq.html
GLR in Coudé spectrograph room
Electronics racks
GDA cryostat
GLR optics bench
Coudé spectrograph room
Electronics racks
GDA cryostat
GLR Optics
Cryo-compressor
Coudé focus
(a)
(c)
(b)
Instrumented historic Hale telescope operated by Caltech Optical Observatories to implement GLR
Tungsten silicide (WSi) superconducting nanowire single photon detector (SNSPD) array
  300 µm in diameter
  Comprised of 64 nanowires configured in 4-quadrants, allowing spatial tracking of downlink
Custom ground laser optical assembly developed for coupling light from telescope coude focus
Spatial acquisition on SWIR camera
Utilize circular polarization of downlink laser beam to split signal to SNSPD array
Narrow bandpass filtering
Time-to-digital converter records photon arrivals sensed by WSi SNSPD array
Time stamps processed with bank of FPGA’s for synchronization, demodulation, de-interleaving, decoding
Elaborate monitor and control system that can allow remotely operating the receiver

## Slide 16
Superconducting Nanowire Single Photon Detectors (SNSPDs) are the highest performing detectors available for time-resolved photon counting
1 Kelvin operating temperature
SNSPD arrays for DSOC are made at MDL: inhouse design, fabrication, and testing at JPL
DSOC detector is a 64-pixel 320-µm diameter active area WSi SNSPD array
4 spatial quadrants with 16 nanowire sensor elements each
Device Operation Concept
Electron microscope detail of 320-µm active area tungsten silicide ( Wsi) superconducting nanowire single photon detector (SNSPD) array
Ground Technology
GLR Technologies (1-of-2)

## Slide 17
GLR Signal Processing Assembly
GSPA Monitor & Control
Ephemeris predict data
Detector centroid estimate
To GLR Monitor and Control
To GLR Optics Assembly
Time and Frequency Reference: Brandywine NFS-220
Data Storage: Dell R740/MD1420
Signal Processing Modules: Xilinx VCU-118
…
Time to Digital Converter (TDC): DotFast TDM800+Supermicro-based Control Computer
GLR Technologies (2-of-2)

## Slide 18
GLT
FLT
GLR
DSOC
MOS
DSN
PSYCHE
MOS
LCH
FAA Feed
COO
PSYCHE
1553
Undock
Laser Uplink
1064 nm
Mission Net
Laser Downlink
1550.12 nm
X-Band/LGA
CHILL
VOCA
TCS
VOCA
Open MCT
/CHILL
/VISTA
Open MCT
/CHILL
/VISTA
L3-Harris
PA Files
FLT
Ops
VOCA
MTIF
Mission Operations (MOS)
Mission operations conducted under Operations Manager oversight, supported by Flight Ops, GLR and GLT leads
  Cream shaded boxes are key DSOC operational nodes
  Auxiliary grayed out boxes are critical for successful DSOC operations
DSOC was in commissioning phase from Oct. 25 – Dec. 12
  In addition to initial one-time activities commissioning allowed more interactive but slower mode of operations
  Needed Psyche staff of be on hand for radiating RF commands
Fully sequenced phase since Jan. 1, 2024
  FLT activities are pre-sequenced and ground activities coordinated
  No staffing from Psyche required for nominal ops

## Slide 19
Date | Activity | Brief Description
10/25/2023 | Cover deployment | Frangibolt deployed; indirect spacecraft dynamics evidence that cover was deployed
10/30/2023 | Power on DSOC | All FLT assemblies powered on successfully; platform characterization data, first undock launch-lock release
11/07/2023 | Exercised first acquisition | Weather prevented beacon uplink; captured PCC frames showing bright earth limb; saw flashes of downlink
11/14/2023 | Initial demo of beacon acquisition and downlink at 6.25 Mb/s | Bulk of contact time gathering calibration data for tuning the downlink pointing control
11/21/2023 | Initial end-to-end demonstration return rates of 6.25, 41.6 and 62.5 Mb/s uplink at 1.8 kbps | OCTL used for up- and downlink; O2O Project Receiver used for decoding downlink
12/5/2023 | Operated at 100 Mb/s and 267 Mb/s returning more than 1 Tb data volume | First time GLR and GLT operated co-operatively per planned concept of operations
12/12/2023 | Downlink at 267 Mb/s for most of the night; transmitted high-definition video; uplink and PCC frame data | There were high thin clouds but both uplink and downlink at Table Mountain and Palomar mountain able to operate
1/2/2024 | Operated link at up to 10.4 Mb/s with OCTL serving as both GLT and GLR | First fully sequenced contact demonstrated; SPE angle was < 6-deg
1/9/2024 | Operated link at 267 Mb/s from 0.37 AU, with Palomar as GLR and OCTL as GLT | Second fully sequenced pass, transferred 4.7 Tbits of data from space 35.6 Mb/s-AU2 link difficulty;
1/16/2024 | Operated link at 200 Mb/s from 0.423 AU with Palomar | Third fully sequenced contact that utilized receivers at al 3 ground stations, Palomar, OCTL and Goldstone
1/30/2024 | Operated at 200 Mb/s from 0.56 AU | Performed tests of adding background noise to validate models and other link experiments
2/13/2024 | Clear skies but Palomar not available tested lowering uplink irradiance | Performed arraying experiments with OCTL and RF-Optical Hybrid
Summary of Activities

## Slide 20
Downlink Performance
5.2 dB
7.6 dB
Downlink performance measured exceeds predictions
  Operated DSOC LTA de-rated at 2 W
Accounting for predicted versus operating margins
  Observed 3 – 4 dB improvement
    2-3 dB from better pointing
    1-dB from reduced FLT losses
Pointing story
  Psyche streams on-board computed GLT, GLR unit vectors to DSOC
  Made gross-offset correction in GLT/GLR vectors early in commissioning
    1.5 mrad for GLT and 20 µrad for GLR
    Monitoring gradual drift and corrections to be updated to contain the offsets within PCC FOV of 256 x 256 µrad
  Regular downlink power scans allow estimating residual bias errors
    Correction of measured bias estimates can be corrected through optical uplink commands
  Pointing jitter assessed from beacon centroid on PCC cross-hairs is benign
w/1-m on ground
w/5.08-m on ground

## Slide 21
Some pointing results
Downlink beam model is fit to power profile detected at a given ground station during FLT downlink scan
Estimated location of peak downlink power at receive station is mapped back to FLT pitch and yaw
Jan. 1, 2024
Example of power scan used to correct pointing bias
  Scan duration 5 minutes
  Estimates generated instantaneously
  Commanding back to DSOC 1 light time
Estimate of pointing jitter
  1 Hz centroid telemetry used
  Working on getting higher sample rate centroid data
Uplink optical command to offset downlink pointing issued at 3:52 UTC
Jan. 9, 2024

## Slide 22
Example
downlink decoding success
Example taken from Jan. 9 spacecraft range 0.37 AU operating at 267 Mb/s
  Occasional decoding failures not related to beacon interruptions, under study
Uplink Laser power
Laser Safety interruptions

## Slide 23
0.2 AU SUM
0.42 AU SUM
0.2 AU MSQ
0.42 AU MSQ
Beacon
DL
Beacon arrived 2-minutes after FLT scan started
Beacon Uplink
Uplink powers used resulted in irradiances
  30-50 pW/m2
  Scanned uplink beam to measure pointing offset and beam divergence
    3-µrad pointing error
    96-rad beam divergence compared to 100+/-10 rad designed 1/e2 uplink divergence
Earth-radiance background 2-3 x higher than estimated
  Does not impact link acquisition when beacon is present
Acquisition times were less than targeted 300 seconds as long as beacon is present at start
Uplink receiver working well
  4.8 Mbytes of error free data volume delivered,
Jan. 1 and Jan. 9, 2024
“Snap-shot” of high-rate (15 kHz) slot counts recorded for measuring uplink scintillation
  Initial estimates made

## Slide 24
Summary and Conclusions
DSOC technology demonstration is off to a great start
  Highest designed data-rate was demonstrated from 0.37 AU with 4.7 Tbits of downlink volume
  Enabled by good pointing control and ability to estimate and feedback pointing bias corrections
Key future objectives are:
  Operate with lower laser uplink irradiance
  Watch thermal health as temperature falls as spacecraft recedes from sun
  Continue to downlink DSOC telemetry and also Psyche or “customer” data
Viability for robust deep space service looks promising
  Require development of daytime, near-sun pointing ground infrastructure
Operating 3 ground stations concurrently deferred to future presentation
  Bonus for the technology demonstration
  Expect to address backend signal processing for ground array configurations
Operated through clouds over Palomar
Operated through clouds over OCTL

## Slide 25
ACKNOWLEDGEMENT
The research was carried out at the Jet Propulsion Laboratory (JPL), California Institute of Technology under a contract with the National Aeronautics and Space Administration
THANK YOU !
ACKNOWLEDGEMENT
DSOC Team
Psyche Mission leadership and team members hve provided invaluable and critical support to enable DSOC
Acknowledge support of Caltech Optical Observatory staff and directorate
All DSOC partners that delivered tested hardware and continue to support as SME’s