## Slide 1: Design, Build, Fly! @ UCI

## Slide 2: Results
#1 in California - #1 UC
#8/99 Globally
“First in the state, top 10 in the world”
Notes: Time: 80 sec

## Slide 3: Mission Summary Ground Mission (1 point) Mission 3 (3 points) Mission 1 (1 point) Mission 2 ( 2 points)
Carrying a payload weight of min. 30% of gross aircraft weight
Minimum payload size of 3”x3”x6”
No payload
3 laps in 5 mins
Design, fabricate, and flight of an unmanned, radio-controlled aircraft to complete 3 flight missions & 1 ground mission.
Presenting: Deepak
Notes: 20 seconds

## Slide 4: Mission Constraints 1. Shipping Box L+W+H = 62” 2. Shipping Box Weight < 55lb 3. M1, M2, M3 Assembly Time < 5 min 4. GM Assembly Time < 10 min 5. Duplicate Set of Wings in Shipping Box 6. Wing set chosen before assembly
Presenting: Deepak
Notes: 25 seconds

## Slide 5: Scoring Analysis
Score Analysis for Mission 3
Score Analysis for Mission 2
Presenting: Rahul
Notes: Time: 30 sec

## Slide 6: Aircraft Sizing Span: 58in Chord: 11in
Mission 2 + Mission 3 Score Comparison
Presenting: Rahul
Notes: Time: 60 sec

## Slide 7: Design Choices
Single boom
Conventional tail
71” span, 9” chord
Tail dragger
Double boom
H-tail
58” span, 11” chord
Tricycle Gear
Presenting: Deepak

## Slide 8: Final Design
Presenting: Luis

## Slide 9: Cont.
Presenting: Luis

## Slide 10: Aircraft Specifications
Presenting: Deepak

## Slide 11: Airfoil Seleciton
Presenting: Deepak
Final Choice: NACA 4416
Sufficient % thickness for spars
High L/D
Easy to manufacture (no sharp/thin TE)

## Slide 12: Shipping Box Modularity
BoxDimensions: 13.00″x12.50″x36.50″
Box Wall Thickness: .25”
Presenting: Deepak
Notes: Time: 45 sec
Due to the AIAA Design Build Fly rules, our aircraft must fit within a shipping box with a sum of dimensions equaling 62 inches. Because of this constraint, a significant focus was placed on modularity during the design phase with the wings, tail and landing gear being removable for storage. We are required to supply our own box and this have freedom as to the exact dimensions we can use so long as it conforms to the 62” rule thus it was determined that a 12.8 by 9.5 by 39.7 inch box was acceptable with a wall thickness of ⅛ inch due to the low weight of the aircraft.

## Slide 13: Antenna & Payload Max Antenna Length: 36” Max Payload Weight: 5lb
Presenting: Luis
Notes: Time: 20 sec
The antenna fixture is a key component for Mission 3. We have our initial concept on the left. It's a 3D-printed component that connects to the wing fore and aft spars and the hole on the top holds the antenna. A major concern with the antenna is the bending moment produced on the wing spars by the antenna drag. So we did a quick simulation that you can see on the right. Using the approximate drag force on the antenna, we can see the stress created on the wing spars. We see that the most deflection occurs along the PVC antenna itself which flexes to about an inch along its length and that the deflection in the wing spars is at most .15 inches and that none of the components like the spars or the fixture experience any yeilding. Now the other major concern with the antenna is the issues in stability and control during flight. The pilots ability to control a longer length antenna is the limiting factor.

## Slide 14: Antenna Fixture Friction fit for antenna Fixture attached to wing spars Antenna attached via clamp Fixture screwed to wing tip Manufacture in 2 parts to add clamp inside Antenna is attached via pressure through screws Fixture is screwed to wing tip Lightest of all 3
Design 1
Design 2
Design 3
Presenting: Luis
Notes: Time: 45 sec
The antenna fixture is a key component for Mission 3. We have our initial concept on the left. It's a 3D-printed component that connects to the wing fore and aft spars and the hole on the top holds the antenna. A major concern with the antenna is the bending moment produced on the wing spars by the antenna drag. So we did a quick simulation that you can see on the right. Using the approximate drag force on the antenna, we can see the stress created on the wing spars. We see that the most deflection occurs along the PVC antenna itself which flexes to about an inch along its length and that the deflection in the wing spars is at most .15 inches and that none of the components like the spars or the fixture experience any yeilding. Now the other major concern with the antenna is the issues in stability and control during flight. The pilots ability to control a longer length antenna is the limiting factor.

## Slide 15: GM Fixture Aluminum 4-Channel Structure Adjustable brackets Can be disassembled
Presenting: Luis
Notes: 25 seconds

## Slide 16: Ground Mission Test
Presenting: Deepak
Test aircraft supported at wing tip
Sand bags loaded on fuselage
Max weight: 24lb
Notes: 25 seconds

## Slide 17: Landing Gear Test
Presenting: Chaz
Buckling Test
Load: 28lb
Dynamic (impact) Asymmetric Landing w/ Payload
Load: 22lb
Notes: 25 seconds

## Slide 18: Assembly Time Test
Presenting: Chaz
Assembly failure for all missions in iteration 1
<5 minutes for all missions in iteration 2
Notes: 25 seconds

## Slide 19: Motor/Prop Test
Presenting: Chaz
Final Selection: V3 X3520 w/ 14x8 propellor
Notes: 25 seconds

## Slide 20: Flight Test
Presenting: Chaz
Iteration 1
M1
Power usage: 275W over 2.5 min @ 50ft/s
M3
Power usage: 350W over 2 min @ 65ft/s
30” antenna
M3
M1
Notes: 25 seconds

## Slide 21: Drag Breakdown
Presenting: Rahul
Notes: 30 seconds

## Slide 22: Mission Performance
Presenting: Rahul
Notes: 30 seconds

## Slide 23: Mission Performance
 | Possible Score | Actualized Score
Mission 1 | 1 | 1
Mission 2 | 2 | 1.21
Mission 3 | 3 | 2.48
Ground Mission | 1 | .1
 | Predicted Performance | Actualized Performance
Assembly (All missions) | Completed | Completed
Mission 1 | 3 laps in 5 min | Completed
Mission 2 | 10 laps in 10 min | 8 laps in 7.5 min
Mission 3 | 40” antenna – 3 laps/2 min | 30” antenna – 3 laps/2 min
Ground Mission | 24lb added | 25lb added
Presenting: Deepak

## Slide 24: Photos

## Slide 25: Video

## Slide 26
Thank You!
Any Questions?