## Slide 1
Trajectory Planning for Autonomous Parafoils in Complex Terrain
Brian Le Floch Resident Engineer
16th Annual ASAT Conference
November 9, 2019

## Slide 2: Acknowledgements
Advisors
  Jonathan How, Richard Cockburn Maclaurin Professor of Aeronautics and Astronautics at MIT
  Louis Breger and Matthew Stoeckle, Technical Staff at Draper
Funded by the Natick Soldier Research, Development and Engineering Center (NSRDEC)

## Slide 3: Outline
Introduction to Guided Airdrop
Overview of Parafoil Guidance
The Rewire-RRT Algorithm
Results and Conclusions
Figure 1: An airdrop mission begins. How will it end?

## Slide 4
Introduction to Guided Airdrop

## Slide 5: What is Airdrop?
Advantage of Guided Airdrop
  Accuracy – lands closer to target!
Figure 3: Guided airdrop with autonomous parafoils
Figure 2: Unguided airdrop

## Slide 6: Guided Airdrop System
Figure 4: Autonomous parafoil with attached payload
Steerable ram-air canopy
Airborne Guidance Unit (AGU)
Payload

## Slide 7: Guided Airdrop GNC
Figure 5: System diagram

## Slide 8
Parafoil Guidance Overview

## Slide 9: Guidance Strategy
Figure 6: Parafoil Guidance Phases

## Slide 10: Terminal Guidance Problem Statement
Assume simplified parafoil dynamics:
  ,
  ,
  ,
  ,
Input
Miss distance
Find that minimizes miss distance from target!

## Slide 11: Existing Terminal Guidance Approach
Band-Limited Guidance (BLG) is a direct optimization approach
Trajectory parameterized by three equally spaced heading rates , ):
  Band-Limited interpolation determines intermediate heading rates
Optimization performed by Nelder-Mead algorithm
Limitations of BLG
  Constrained trajectory shape
  Slow convergence in presence of obstacles

## Slide 12
The Rewire-RRT Algorithm

## Slide 13: Rapidly-Exploring Random Trees
Advantages
  No preconceived notion of trajectory shape
  Rapidly explore large state-space
  Alternative trajectories available
x0 (root)
x1
d
xnear
xrand
xnew
Introduced in 1998 [LaValle]
Incremental construction of a tree of trajectories

## Slide 14: Parafoil-RRT
RRT was adapted to parafoil guidance problem
Figure 7: Tree of trajectories formed by Parafoil-RRT
Disadvantages
  Consistent but poor miss distance; RRT is guaranteed suboptimal [Karaman et al]
  Unsafe proximity of trajectory to terrain/obstacles

## Slide 15: Solution 1 of 2 (Safety)
Use Analytic Chance Constraints [Luders et al] to estimate probability of collision
  Uncertain winds yield distribution of possible future states
Total cost is weighted sum of safety and miss-distance costs
Two-part cost considers safety and miss-distance
Figure 8: Collision probability region [Luders]

## Slide 16: Solution 2 of 2 (Performance)
Adapt two methods from RRT* [Karaman et al]
  Choose-Parent
  Rewire
RRT* is asymptotically optimal, but can be hard to implement for underactuated systems
Figure 9: RRT (left) vs. RRT* (right)
[Karaman]

## Slide 17: Solution 2 of 2 (Performance) Choose-Parent Procedure
x0 (root)
x1
d
xnear
qnew
xrand
x0 (root)
x1
d
xnear
qnew
xrand
rb
c1
c2
c2 < c1
re
RRT
Rewire-RRT
xnew
xnew
Choose-Parent improves trajectory quality when new nodes are added to the tree
17

## Slide 18: Solution 2 of 2 (Performance) Rewire Procedure
RRT*
Rewire-RRT
rb
x0 (root)
x1
x2
x3
x4
x5
x6
xnew
rb
x0 (root)
x1
x2
x3
x4
x5
x6
xnew
re
c2
c2 < c1
c1
xcandidate
c2
c1
c2 < c1
Rewire improves trajectory quality within the existing tree

## Slide 19
Results and Conclusions

## Slide 20: Static Planning Setup
50 trials per algorithm
Three seconds of tree growth
Evaluate lowest-cost path in tree
Figure 10: Simplified urban drop-zone with buildings and bridge

## Slide 21: Static Planning Results
Mean miss distance for Rewire-RRT is reduced 29%
Figure 11: RRT (left) vs Rewire-RRT (right)

## Slide 22: Simulation Setup
Monte-Carlo simulations of entire flight profile
Utilizes Draper’s extensively verified parafoil simulator
50 trials per algorithm
Figure 11: Simplified urban drop-zone for simulation experiments

## Slide 23: Simulation Results
Demonstrated improvements with Rewire-RRT:
  Mean miss distance reduced 9%
  Miss distance at 80th percentile improved 22.9%
Figure 11: Cumulative density function of normalized miss distance

## Slide 24: Conclusions
Rewire-RRT is a sampling-based parafoil path-planner that explicitly minimizes the risk of collision with obstacles along each path and minimizes the expected final miss distance from the target.
Contributions:
  Novel cost function considering the airdrop objectives
  A fast, analytic method to rewire the tree for the under actuated parafoil system
  Simulation results that demonstrate the ability of Rewire-RRT to find better paths through the environment than RRT and CC-RRT.

## Slide 25: References
LaValle, Steven M. "Rapidly-exploring random trees: A new tool for path planning." (1998).
Luders, Brandon D., Ian Sugel, and Jonathan P. How. "Robust trajectory planning for autonomous parafoils under wind uncertainty." AIAA Infotech@ Aerospace (I@ A) Conference. 2013.
Karaman, Sertac, and Emilio Frazzoli. "Sampling-based algorithms for optimal motion planning." The international journal of robotics research 30.7 (2011): 846-894.
Le Floch, Brian, et al. "Trajectory Planning for Autonomous Parafoils in Complex Terrain." 24th AIAA Aerodynamic Decelerator Systems Technology Conference. 2017.

## Slide 26
Thank you!
Questions/Comments?