## Slide 1: Effect of End Fixity Modeling on Vibration Behavior of Bolted Components
Background Information
Boundary conditions for bolted joints are usually modelled as fixed constraints at bolt holes.
Three approaches are discussed for modeling bolted joints:
  Fixed constraints at bolt holes
  Explicit modeling of bolts and attachment
  Fixing remote points associated with bolt holes
Component simplified as cantilevered cylinder with end flange attached with four bolts
Modal and random vibration results are compared for the three approaches
EAC
Engineering Analysis Consultants

## Slide 2: Modal Analysis of Component with Fixed Constraints at Bolt Holes
First Six Modes with Holes Fixed

## Slide 3: Acceleration & Stress Response to Random Vibration
Max. Acc. PSD Response = 9.01 G2/Hz
Max. Equiv. Stress = 5.1 KSI
Input Accel. PSD

## Slide 4: Modal Analysis of Component with Explicit Bolts & Fixture (High Level Excitation)
First Six Modes with Explicit Bolts & Fixture

## Slide 5
Acceleration & Stress Response to Random Vibration
Max. Acc. PSD Response = 9.08 G2/Hz
Max. Equiv. Stress = 5.6 KSI
Input Accel. PSD

## Slide 6: Modal Analysis of Component with Explicit Bolts & Fixture (Low Level Excitation)
First Six Modes with Explicit Bolts Intact

## Slide 7: Acceleration & Stress Response to Random Vibration
Max. Equiv. Stress = 5.1 KSI
Max. Acc. PSD Response = 8.89 G2/Hz

## Slide 8: Modal Analysis of Component with Remote Points
First Six Modes with Remote Points

## Slide 9
Acceleration & Stress Response to Random Vibration
Max. Equiv. Stress = 6.2 KSI
Max. Acc. PSD Response = 8.76 G2/Hz

## Slide 10: Conclusions
Fixing bolt holes leads to unconservative stress response
Explicit modelling of bolts, while more laborious, produces higher and more realistic stress estimates.
Remote point approximation will predict higher stresses and lower accelerations
Fixing bolt holes may be acceptable for low excitation levels as the bolts will remain tightened.
For higher excitation level explicit bolt modelling is recommended.
For low level excitation higher contact stiffness bolted connection results approach fixed hole constraint results.